## Slide 1: Auditory Mechanisms for Spatial Hearing
J.D. (jj) Johnston
Immersion Networks

## Slide 2: Questions?
Please ask questions in the chat.
I may ask you to defer a question until later, be sure to remind me later if I fail to get to the answer, or if it wasn’t obvious to you.
I’m not talking specifics today. The amount of data required to convey specifics is more like a semester’s worth.

## Slide 3: First, a review of what one ear can do.
The ear is a frequency sensitive organ.
  The filter structure is unique to the ear, and unlike what most people expect.
  The detectors come after the filter structure.
  Yes, the filter mechanism on the basilar membrane is well supported.
The detectors work differently at different frequencies
  At low frequencies (under 500Hz), they fire at the start of the waveform itself, as filtered on the cochlea.
  At high frequencies, (over 2000Hz or so), they fire at the start of the waveform envelope.
  The firing rate is also proportional to loudness, so more firings happen with louder stimuli.
  Yes, at mid-frequencies, the two mechanisms conflict.

## Slide 4: Frequency Sensitivity
For a mechanism discussion, please see my previous talk at https://www.aes-media.org/sections/pnw/pnwrecaps/2019/apr2019/
There are about 3500 inner hair cell clusters. Each cluster has a bandwidth of about 1 erb, although it is wise to remember that the filter is not symmetric about the center frequency.
An ERB is approximately 40 to 50Hz at low frequencies, and about ¼ octave at frequencies where ¼ octave exceeds 40 to 50 Hz.
Inner hair cells (the detectors) are roughly placed uniformly along the ERB scale. (disregarding hearing damage and other issues)

## Slide 5: The filters are not symmetric.
Due to the mechanisms that create the filters, a filter is more sensitive to frequencies below the center frequency than it is to frequencies above the center frequency.
The cutoff toward lower frequencies is about 25dB/ERB once you are past ½ ERB below the center frequency, and varies with the SPL of the sound input.
The cutoff toward higher frequencies, once you are past ½ ERB above the center frequency, is incredibly steep. This is due to the basic filtering mechanism.

## Slide 6: The combination of filter and detector is not linear.
Signals within the filter bandwidth interact with the filterbank structure via outer hair cells to compress the loudness sensation as compared to the actual level input.
  This means that an increase of 10dB in signal level raises the loudness by a factor of about 2.
  Signals outside a given filter bandwidth do NOT cause the signal in that bandwidth to compress!
  There is a 1 millisecond or so delay at the onset of the compression.
    ATTENTION, this means the leading edge is emphasized. This will be important later.
  Loudness ADDS across different ERB’s, but compresses inside an ERB. The compression level for addition is different than the overall 2x per 10dB.
  Remember: Loudness is the perceived intensity. SPL or level is the measured signal level. No, they are not the same thing.

## Slide 7: Loudness vs. Intensity
The compression on the cochlea due to the interaction between inner and outer hair cells maps the 30dB dynamic range of the inner hair cell to more like a 100dB dynamic range.
As levels rise, the bandwidth of the filters becomes larger. This does affect things like articulation and interaural time sensitivity
  Articulation is worse
  Time sensitivity is somewhat increased.
Compression starts under a millisecond after the inner hair cell firing.
Compression releases more slowly, with several very difficult-to-determine time constants that also vary with frequency.

## Slide 8: What comes out of the detectors?
Firing rate (measure of loudness in a given frequency range)
Start of signal in that frequency range (for any frequency)
For low frequencies, waveform lock.
For high frequencies, leading edge of envelope lock
For mid frequencies, you get some of each of waveform and envelope. This does manifest later as lesser delay detection in that range of frequencies.

## Slide 9: So, we have two ears. Now what?
We can compare time relationships between the two ears, to the level allowed by what the detectors capture, which is to say, waveform under 500Hz, a mix of waveform and envelope between 500Hz and 2kHz (yes, there is synchronous firing beyond that point, but it is generally overwhelmed by envelope variation), and envelope leading edge above 2kHz. This is called interaural time difference. (ITD)
The leading edges (in time) in an ERB will be emphasized relative to the steady state due to the onset of compression. (One of the facets of Haas effect)
The interaural level difference between the two ears will be communicated to the brain.

## Slide 10: The acoustics of the head
The acoustic signals in a room come from a variety of sources.
  The direct signal from a non-occluded source
  Reflections of the direct signal from surfaces. Remember that the source itself is usually directional!
  The reverberant signal (for rooms with substantial reverberation).
    It has been proposed that reverberant signals are orthogonal at the two ears, i.e. they are uncorrelated.
    There are many ways to create uncorrelated signals.
    Some of them sound like reverberation
    Some of them just sound weird.
    The use of the analytic measure of cross-correlation is not really the right metric here, but that’s a lightning rod. I’m going to ground that for now.

## Slide 11: The path to the ear canal.
As has been discussed over and over by now, the path to the ear affects the impulse response, time delay, and frequency response of a sound source. This is called the HRTF or HRIR (same information, in either frequency (HRTF) or time (HRIR) domains. HR means “head related”, TF is “transfer function”, and “IR” is impulse response.
Reflections typically come from different paths than the direct sound.
Reverberation is usually diffuse (although standard stage/hall concert halls actually have two directions for reverberation in many cases, for good halls.

## Slide 12: Definitions:
ITD: Interaural time delay (A function of direction, distance, and frequency), denoted by f, r, theta, and phi
ILD: Interaural level difference (Also a function of direction, distance, and frequency), denoted similarly
F – frequency in Hz, or alternately omega, frequency in radians/second.
R – radius, distance from source to the midline between the ears.
Theta – Horizontal angle of incidence
Phi – Vertical angle of incidence
Cone of Confusion: A roughly cone-shaped surface over which mean ITD is the same.

## Slide 13: So, the direct sound is just what comes out of the source?
Well no, not really.
The source is often (usually, almost always) directional.
Wind, air flow, air currents, eddies, etc, actually affect the direct sound at any appreciable distance.
Air is nonlinear. Things like percussion, some brass, and the like will have spectral changes as you move away from the source due to this nonlinearity.
Just taking a close-miked capture and assuming the result is the same at distance is going to surprise you even in a room without much reverberation for signals with high peak amplitudes.

## Slide 14: So about this direct sound diffusion thing?
Yes, there is some diffusion on the direct sound. Not a lot, but it can affect sensation quite a bit, as well as blur directional sensation (by making ITD a bit noisy).
This diffusion is very hard to model, it’s basically similar to a Rayleigh process (although not quite, of course). More will not be said here.
To some extent, this is related to some of the calls for “decorrelation”, however, there are an infinite (literally) number of ways to decorrelate, and most of those do not sound right. Some of them, in fact, sound extremely strange. (I will not pass along some subjects’ descriptions here.)

## Slide 15: So, what happens to the direct sound?
Well, the direct sound is affected by the appropriate HRTF or HRIR (same thing, different domains) so to speak, and delivered to the ear. This does provide the primary location on the cone of confusion (a more or less cone-shaped place where ITD is constant.
  Of course, ITD can and will vary over frequency (only by a little bit, but it matters), which can somewhat disambiguate elevation in the cone of confusion.
  ILD will help disambiguate the elevation, as will differences in ILD between the two ears.
The direct sound always gets there first, when there is a direct sound (no occlusion)

## Slide 16: Direct gets there first!
Recall, if you will, that auditory compression starts about 1 millisecond after onset.
This helps “emphasize” the direct sound, because it does come first.
Even in a reverberant environment, this can provide surprisingly useful directional cues.
Why is this important?
  It lets us hear “through” reverberation
  It can be integrated with eyesight to understand speech in a bad environment, by capturing the peaks that are above the noise/reverberant floor.
  Interaurally, the brain can also reject “decorrelated” signals around frequencies present in the direct signal’s peaks.
This presumes the direct sound does not have a flat envelope at high frequencies. At low frequencies, some degree of phase lock still works.

## Slide 17: So, then, why is it so hard to localize a high frequency tone?
Well, first, it’s a tone. It has a flat envelope, so there is no “first arrival” information
It’s a high frequency, and will reflect off of small surfaces. Many small surfaces, in fact.
The reflections will interfere with each other, and with the ITD arising from HRTF’s.
That’s almost impossible to localize, indeed.
Yes, smoke alarms should make a short series of beeps, not just one, when they are running out of battery!

## Slide 18: On to (early) reflected sound
First, timbre from different directions from an instrument, voice, machine, or most anything may be strikingly different.
  Think about a helicopter flyover.
  Walk around a brass player and listen to the timbre.
The sound from reflected sound sources will reflect the timbre of the sound source.
Reflections can either enhance or destroy localization, depending on the kind, amplitude, and spectrum.
Early, here, refers to longer path lengths of a few meters (maybe up to 4-5 meters)

## Slide 19: Remember, reflections arriving at the ear will reflect the HRTF due to their direction.
Note, this is concerning specular (non-diffused) reflections. More on diffusion later.
As a result, early reflections can affect timbre, localization, and width of the source.
NOTE: This is not referring to the “reflections in 2-channel rendering” which are reputed to do a number of things:
  They may aid the phantom image (done right)
  They may destroy the phantom image (see above)
  They may (usually adversely) affect timbre.
  This issue comes about much later in the auditory system, and will not be discussed today. Sorry.

## Slide 20: Diffused reflections
Diffused reflections will have their leading edges across frequency somewhat scrambled, and as such, tend to have fewer ‘leading edge’ behaviors.
Diffused reflections will add to the loudness of the main source in most cases.
Diffused reflections may create a sense of distance, but will not usually mess up timbre.
Too much diffused reflection, of course, is possible.
HRTF applied to the diffuse reflection, of course, will correspond to the path from the diffusor to the listener.

## Slide 21: Late Specular Reflections
Are generally bad news.
Can garble articulation.
Create echoes over 50 millisecond delays or so.
Late reflections, effectively create new “leading edges”, and the problems follow from there.

## Slide 22: Reverberation
For the purpose of this discussion, reverberation refers not only to stored energy in the room that adds incoherently in the mathematical sense, but also a collection of (potentially frequency shaped) reflections that happen rapidly in close succession such that cochlear compression does not release.
  I say this because there are endless arguments about when the end of “late reflections” of high time density becomes “true reverberation”.
  Likewise, debates about the Schroeder Frequency are outside of the scope of this discussion and will provoke endless debate, some of which ignores time scope and stationarity of reverberation.
This definition includes what the EAR will resolve as reverberation.

## Slide 23: Timbre of direct vs. reverberated sound
For signals that have substantial time-domain character, the timbre difference between the direct and the later reverberant sound can also disambiguate front from back.
  That’s because pinna shadow means the HRTF from the back is missing a lot of high frequency
  The reverberation, being from ‘all around’ is not suffering from the same amount of HF loss, but reverberation does tend to have less treble than the direct sound (for front or especially side) in general.
  To the extent it works, this is how front/back disambiguation works.

## Slide 24: HRTF’s
There are many HRTF’s available these days on the web
HRTF’s are, unfortunately, not “one size fits all”
I’m not going to show one set of HRTF’s, rather I’ll describe the basic trends.
HRIR’s are simply the same information, in the time domain.

## Slide 25: Horizontal trend in HRTF/HRIR
Typically, high frequencies are strongest when the source is pointed straight into the ear canal.
At angles other than that, two paths around the head can place either one or two near-zeros in the response.
Far side HRTF’s magnitude is substantially smaller above bass and low midrange frequencies.
Elevation of source in the HRTF depends substantially on ear-shoulder distance. That’s an entire talk in itself.
Depression of source direction involves body shadowing, and is in the same state as elevation of course.

## Slide 26: Hearing for very diffuse signals.
First, very diffuse signals (reverberation) can be regarded as coming from all directions, so there is a “diffuse” HRTF/HRIR to be considered.
Second, and this is very important, the arrival time in a given ERB will be scrambled (and different) between the two ears across frequency. This is important to the perception of “diffuseness”. This scrambling in ERB’s does determine to some extent actual sensation of the reverberation.
The SAME time delay across channels (i.e. one reverb) over many ERB’s is certainly a known issue. Yes, 1950’s practice remains right and we know why for sure, now.

## Slide 27: Distance perception
As discussed above, the direct signal can be detected surprisingly well even with an overall reverberation that contains more energy, because of the peaks rising above the reverberation.
  Of course, at some point the direct signal breaks down, and localization is then only via ILD
  Little reverb (high signal to reverb ratio) is close
  Lots of reverb (low signal to reverb ratio) is far away
  How far depends entirely on the characteristics of the reverb (bigger rooms, longer T60, longer distance even for the same direct/reverb ratio.
Wait, there’s more. There’s the effect of transmission across distance.

## Slide 28: What about the effect of air currents, etc?
This effect moves around the arrival time, varying both by ear, and by source and distance.
  This kind of diffusion is tricky.
  It is not merely “partial decorrelation”. There is an infinite number of ways to decorrelate (partially or completely) two signals. Many of these do not do the right thing.
  This is a primary source of externalization for headphone wearers.
    I can’t say more on that today.
The more decorrelation of leading edge across frequency, the farther away something sounds.

## Slide 29: Headphone virtualization
Obviously, one tries to mimic the HRTF of the listener, given source direction and distance (yes, ILD and ITD vary with distance as well as frequency).
One must add some sense of space (reverb).
  This must be perceptually diffuse
  This does not have to be mathematically diffuse at all.
  Not all mathematically diffuse things are perceptually diffuse.
  It is essential to have separate diffusion for the two ears.
  That gets you distance.
You must provide a minimum amount of diffusion in order to properly externalize. Again, I can’t say more at the minute.

## Slide 30: To summarize
Recognizing acoustics and transmission path effects are key
HRTF’s/HRIR’s need at least some customization
Structure of room reverb, room reflections, artificial reverb, and artificial reflections are very important.
Remember the emphasis on first arrival above 2K
Remember the phase-lock effect below 500Hz
Remember some of both in the range 500Hz to 2K, obviously moving from mostly phase lock to mostly first arrival of envelope

## Slide 31: Questions?